## Slide 1: Predictive Maintenance for the Smart Factory
AI FOR INDUSTRY 4.0
A machine-learning system that predicts industrial machine failures before they stop the line.
10,000
sensor records
0.98
ROC-AUC
79%
failures caught
75.8%
cost saved
Yousef Abdallah Khamis | AI & Machine Learning Engineer

## Slide 2: From reacting to predicting
01 THE PROBLEM AND THE IDEA
10,000
machine records analysed
3.39%
are failures: a needle in a haystack
50,000 EGP
assumed cost of one unplanned stop
Reactive maintenance (today)
Predictive maintenance (this project)
Fix the machine after it breaks
Unplanned line stoppage
Cost on test set: 3.4M EGP
Sensors feed a model that outputs a risk score
Service only machines at risk
Cost on test set: 0.82M EGP

## Slide 3: The AI4I 2020 dataset
02 INPUTS
Sensors (5)
Air temp [K], Process temp [K], Rotational speed [rpm], Torque [Nm], Tool wear [min]
Product type
L (60%), M (30%), H (10%) quality variants
Identifiers
UDI and Product ID: dropped before modelling
Labels
Machine failure plus 5 modes: TWF, HDF, PWF, OSF, RNF
Target: Machine failure
Chart: 
| No failure | Failure
Target | 9661 | 339
Imbalance ratio about 28 : 1

## Slide 4: Six steps from raw data to decisions
03 HOW IT WORKS
1
Load and inspect
10,000 rows x 14 columns, 0 missing values, 0 duplicates
2
Explore (EDA)
Target imbalance, failure modes, correlations, box plots
3
Feature engineering
5 physics-based features + type encoding = 11 inputs
4
Split and SMOTE
80/20 stratified split; SMOTE on train only: 8,000 to 15,458
5
Train 3 models
Logistic Regression, Random Forest, XGBoost
6
Explain and value
SHAP, Isolation Forest, cost-benefit in EGP

## Slide 5: Five steps in Google Colab
04 HOW TO RUN IT
1
Upload archive.zip (contains ai4i2020.csv) to Google Drive
2
Open the notebook in Colab and mount Drive
3
Install the requirements (xgboost, shap, imbalanced-learn)
4
Run cells 1 to 10 in order
5
Download predictive_maintenance_project.zip
$ pip install -r requirements.txt
pandas numpy matplotlib seaborn
scikit-learn imbalanced-learn
xgboost shap joblib
fastapi uvicorn
# training time (CPU)
Logistic Reg. 0.18 s
Random Forest 7.69 s
XGBoost 0.55 s

## Slide 6: Physics turned into features
05 FEATURE ENGINEERING
Temp_Difference
Process temp - Air temp
Cooling efficiency
Power_W
Torque x RPM x 2pi / 60
Mechanical power in watts
Tool_Stress
Tool wear x Torque
Load on the cutting tool
Wear_per_RPM
Tool wear / (RPM + 1)
Wear per rotation
Thermal_Load
Temp_Difference x Power_W
Heat generated under load
Plus Type_Encoded (H=0, L=1, M=2) = 11 model inputs. Three of the top-5 SHAP features are engineered.

## Slide 7: XGBoost wins on balance
06 RESULTS
Chart: 
| Accuracy | Precision | Recall | F1-Score | ROC-AUC
Logistic Regression | 0.8645 | 0.1838 | 0.8676 | 0.3033 | 0.936
Random Forest | 0.9745 | 0.5859 | 0.8529 | 0.6946 | 0.9855
XGBoost | 0.9795 | 0.6667 | 0.7941 | 0.7248 | 0.9809
XGBoost: selected model (best F1)
97.95%
Accuracy
79.4%
Recall
0.725
F1-Score
0.981
ROC-AUC

## Slide 8: Where the model is right and wrong
07 ANALYSIS (1/2)
1,905
True negative: healthy, correct
27
False positive: false alarm
14
False negative: missed failure
54
True positive: failure caught
Catches 54 of 68 real failures (79% recall)
27 false alarms among 1,932 healthy cases (1.4%)
14 failures missed. Lowering the 0.5 threshold would trade precision for recall
Isolation Forest flagged 120 samples but found only 34 of 68 failures: a complement, not a replacement

## Slide 9: Why the model decides: SHAP
08 ANALYSIS (2/2)
Top-5 drivers (mean |SHAP|)
Tool wear [min]
1.55
Rotational speed
1.32
Power_W *
1.09
Temp_Difference *
0.89
Tool_Stress *
0.65
* engineered feature. Physics-based features rank among the top drivers, so the model learned real mechanics rather than noise.

## Slide 10: What the model is worth
09 BUSINESS IMPACT
Projected annual cost (million EGP)
Chart: 
| Without AI | With AI
Cost | 41.37 | 9.99
75.8%
maintenance cost reduction
31.4M EGP
saved per year (extrapolated)
Assumptions (editable): 50,000 EGP per unplanned failure, 2,000 EGP preventive fix, 500 EGP per false alarm; the 2,000-sample test set stands for one month.

## Slide 11: What the project delivers
10 OUTPUTS
xgboost_model.pkl
Trained classifier, 440 KB
scaler.pkl
StandardScaler for new data
features.json
The 11 input features
results.json
Metrics of all 3 models
summary.json
Best model, savings, top features
requirements.txt
Python dependencies
README.md
Project documentation
project .zip
Everything in one download
Real-time risk score
Risk > 0.5 triggers an ALERT
Sample
Risk
Status
354
0.006
OK
569
0.012
OK
1903
0.006
OK
663
0.000
OK
Examples from the notebook demo (10 random test samples, all healthy and correctly scored).

## Slide 12: Honest strengths and limits
11 PROS AND CONS
Strengths
Catches 79% of real failures early
98% accuracy, ROC-AUC 0.98 on unseen data
Explainable: SHAP shows why an alert fires
Fast: XGBoost trains in 0.55 s on CPU
Clear ROI: 75.8% lower cost
Limitations
Precision 0.67: about 1 alert in 3 is false
14 of 68 failures still missed
Synthetic dataset: validate on real plant data
EGP costs are assumptions; one split, no tuning
Isolation Forest is weak (34 of 68)

## Slide 13: From notebook to the factory floor
12 HOW TO USE IT
Production lines
Score CNC and milling machines continuously
Maintenance plans
Service by risk, not by calendar
Spare parts
Stock tools before they wear out
Safety and quality
Fewer sudden breakdowns and defects
Phase 1: Pilot
One line, offline scoring, tune the alert threshold
Phase 2: Integrate
FastAPI service + SCADA/MES feed + dashboard
Phase 3: Scale
Retrain on plant data, monitor drift